## Slide 1
Golden Model
Deep Dive
SimX C++ Reference Model Integration with UVM via DPI-C for Vortex GPGPU
What is a Golden Model?
SimX: The Right Choice
C++ vs SV
7 Integration Methods
Why DPI-C Won
DPI-C Internals
UVM Architecture
File-by-File Breakdown
Vortex GPGPU Verification Team · 2025

## Slide 2
SECTION 1
What is a Golden Model?
Golden Model (Reference Model): A functionally correct, trusted software representation of the DUT that produces expected outputs. It is the single source of truth in a verification environment — the answer key.
VERIFICATION FLOW
Test Stimulus
▶
DUT
(Vortex RTL)
▶
Golden Model
(SimX C++)
▶
Scoreboard
(Compare)
▶
PASS / FAIL
Actual Outputs
Expected Outputs
KEY INSIGHT
Both DUT and Golden Model receive IDENTICAL stimulus. The Scoreboard compares their outputs — any mismatch is a bug.
5 REASONS IT'S IRREPLACEABLE
① Defines Correctness
② Enables Regression
③ Covers Corner Cases
④ Documents Design Intent
⑤ Critical for GPU Complexity

## Slide 3
SECTION 1
8 Required Properties of a Good Golden Model
A
Functional Correctness
Correct RISC-V ISA execution including F/D/M/A/C/Zicond, SIMT warp/thread semantics (vx_tmc, vx_split, vx_bar), memory model & CSR behavior.
B
ISA-Level Abstraction
Must NOT model pipeline stages or cache timing. Only architectural state: registers, memory, PC, CSRs — independent of microarchitecture.
C
Independence from RTL
Developed completely separately. If written from same logic, bugs in one mask bugs in the other. SimX is a standalone C++ simulator.
D
Performance
Must execute faster than RTL simulation. RTL runs at ~1 KHz–1 MHz. Behavioral C++ models run orders of magnitude faster.
E
Observability
Must expose interfaces to read internal state: register file, memory, PC values, CSR values, execution traces.
F
Completeness
Must handle ALL instructions the DUT can execute. An incomplete model that skips certain instructions is dangerous.
G
Determinism
Given identical inputs, must always produce identical outputs. Non-deterministic behavior makes debugging impossible.
H
Clean Interface
Must expose: initialize, load programs/data, configure CSRs, step execution (by instr/cycle/completion), read back state, reset.

## Slide 4
SECTION 2
Can We Use Something Other Than SimX?
INSUFFICIENT
Spike
RISC-V ISA Simulator
✓ Complete RISC-V scalar ISA; official & trusted
✕ No SIMT execution model; no Vortex custom instructions (vx_tmc, vx_wspawn, vx_split, vx_bar); would need full rewrite
UNSUITABLE
QEMU
RISC-V Target
✓ Widely used system emulator
✕ System-level emulator with Linux OS overhead; no SIMT model; no Vortex custom instructions; wrong abstraction level
WRONG PURPOSE
Verilated RTL
via Verilator
✓ Cycle-accurate; already used in Vortex build system
✕ CRITICAL FLAW: Not independent — if RTL has a bug, Verilated model has the same bug. You'd compare RTL to itself.
CORRECT CHOICE ✓
SimX
Vortex Functional Simulator
✓ SIMT semantics, all custom instructions, full DCR model, same config system as RTL, validated across thousands of tests
✕ None — this is the definitive choice

## Slide 5
SECTION 2
7 Reasons SimX is the Definitive Choice
1
Vortex-Specific SIMT Semantics
Handles vx_tmc, vx_wspawn, vx_split, vx_bar, vx_pred — custom GPU thread control instructions that no external simulator supports.
2
Co-Designed with the RTL
Developed by the same Vortex team, independently. Every ISA extension in the RTL has a corresponding SimX implementation updated in parallel.
3
Same Configuration System
Reads from VX_config.h — the exact same config header as the RTL. Change NUM_WARPS or NUM_CORES and BOTH are configured identically through compiler -D flags.
4
Institutionally Trusted
Vortex research papers use SimX output as ground truth for RTL correctness validation. Years of institutional trust and thousands of validated test programs.
5
Rich Memory & DCR Model
Models full Vortex memory system: RAM abstraction, startup address, and Device Configuration Registers. No external tool models this.
6
Already Validated
Validated against thousands of Vortex tests. You inherit trust — not building it from scratch.
7
Performance: 100×–1000× Faster
Functional (non-cycle-accurate) simulator. Executes programs dramatically faster than cycle-accurate RTL simulation — essential for regression throughput.
SimX is the ONLY complete functional simulator for Vortex GPGPU — no alternative comes close.

## Slide 6
SECTION 3
C++ vs SystemVerilog: The Golden Model Language Choice
✓ YES — Using C++ for golden models is the industry-standard best practice. It is the PREFERRED approach in virtually all serious verification methodologies.
ASPECT
C++ (SimX)
SystemVerilog
C++ (SimX) ✓
Abstraction Level
ISA/functional level — no clock concept
Forces cycle-level execution model
Speed
Native CPU speed (billions of ops/sec)
Simulator speed (MHz range)
Ecosystem
Full STL, GDB, Valgrind, profilers
Limited to simulator toolchain
Data Structures
std::vector, std::map — perfect for memory/regs
Arrays only, no dynamic allocation
Reusability
Standalone executable, testable independently
Simulator-dependent, no standalone use
Integration Mechanism
DPI-C (IEEE 1800 standard)
Native SV (also standard)
Appropriate for GPGPU
YES — the correct abstraction level
NO — wrong execution model
Industry Examples: ARM Fast Models (C++), NVIDIA GPU simulators (C++), Spike for RISC-V (C++), gem5 (C++) — all use DPI-C to integrate with UVM.

## Slide 7
SECTION 4
7 Methods to Integrate C++ Golden Models with UVM
PLI
1980s–1990s
DEAD
VPI
IEEE 1364-2001
WRONG TOOL
FLI
ModelSim Prop.
VHDL ONLY
SystemC TLM
IEEE 1666
OVERKILL
IPC / Shared Mem
POSIX
HIGH OVERHEAD
File-Based
Pre-DPI Era
NO RANDOM
DPI-C
IEEE 1800-2005
WINNER ✓
Oldest
Newest / Best →
IEEE Standard
Each method will be detailed on the following slides →
RELATIVE CALL OVERHEAD
PLI
~200–800 ns
VPI
~1,000 ns
IPC
~5,000 ns
SystemC
~200–800 ns
DPI-C
~5 ns (direct call)

## Slide 8
SECTION 4
Methods 1, 2 & 3: PLI · VPI · FLI
Method 1: PLI
Programming Language Interface · IEEE 1364-1995
HOW IT WORKS
C code registered via global table. Called from Verilog as $simx_run. TF/ACC routines for data exchange.
PROS
✓ Available in all 1990s simulators
✓ Simple concept for basic tasks
CONS
✕ No type checking — buffer overflows common
✕ No SystemVerilog support whatsoever
✕ No C++ support — C only
✕ Completely obsolete since IEEE 1364-2001
VERDICT: IMPOSSIBLE for SimX — requires C++17 features.
Method 2: VPI
Verilog Procedural Interface · IEEE 1364-2001
HOW IT WORKS
Unified C API for simulator database access. C code reaches INTO simulator via vpi_handle, vpi_get_value. Registers callbacks on events.
PROS
✓ IEEE standardized, all major simulators
✓ Can access ANY sim object (signals, params)
✓ Good for RTL monitors and checkers
CONS
✕ Extremely verbose: 10–20 lines per simple call
✕ Slow: every call traverses sim's DB with string lookup
✕ Passing byte arrays = per-byte vpi_scan calls
VERDICT: Theoretically possible, but wrong tool — extremely painful & slow.
Method 3: FLI
Foreign Language Interface · ModelSim/Questa Proprietary
HOW IT WORKS
Mentor proprietary extension to VHDL simulation (ModelSim/QuestaSim). Uses foreign attribute to bind VHDL procedures to C functions.
PROS
✓ Well-supported in QuestaSim
✓ Simpler than VPI for basic calls
CONS
✕ VHDL ONLY — entire UVM testbench is SystemVerilog
✕ Questa/ModelSim ONLY — zero portability
✕ Proprietary, not standardized
VERDICT: IMPOSSIBLE — SV testbench cannot call FLI.

## Slide 9
SECTION 4
Methods 4, 5 & 6: SystemC TLM · IPC / Shared Memory · File-Based
Method 4: SystemC TLM
IEEE 1666 · Two-Kernel Cosimulation
HOW IT WORKS
Wrap SimX as a SystemC module. Two simulation kernels run in lockstep: the QuestaSim kernel and the SystemC kernel, synchronized at defined interfaces.
PROS
✓ IEEE standard (IEEE 1666-2011)
✓ Natural fit for C++ models
✓ Reusable across sim/emulation/FPGA
✓ Used by ARM Fast Models
CONS
✕ Requires Questa SystemC license (extra cost)
✕ Two kernels = 20–50% slowdown
✕ Overkill for ISA-level model (clocks/ports not needed)
✕ Massive complexity to wrap SimX in SystemC modules
VERDICT: OVERKILL — Unnecessary complexity for ISA-level model.
Method 5: IPC / Shared Memory
POSIX Sockets · Pipes · Shared Memory
HOW IT WORKS
SimX runs as a separate process. UVM communicates via shared memory, named pipes, or Unix sockets. Semaphores synchronize the two processes.
PROS
✓ Process isolation — SimX crash doesn't kill QuestaSim
✓ Can run SimX on separate hardware
✓ Independent debugging with GDB
CONS
✕ IPC overhead per call (~5,000 ns vs DPI-C ~5 ns)
✕ Synchronization complexity — race conditions hard to debug
✕ Cannot integrate naturally with constrained-random UVM
VERDICT: HIGH OVERHEAD — Poor complexity-to-benefit ratio for software sim.
Method 6: File-Based / Offline
Pre-DPI Era · Directed Tests Only
HOW IT WORKS
Run SimX offline, dump outputs to files (hex, CSV). UVM test reads files and compares. All golden results pre-computed before simulation.
PROS
✓ Zero integration complexity
✓ Perfect isolation
✓ Human-readable files, easy debugging
✓ Works with any simulator
CONS
✕ NOT dynamic — can't work with constrained-random UVM
✕ Post-mortem only — no on-the-fly comparison
✕ Cannot handle stimuli generated at runtime
VERDICT: NO RANDOM STIMULUS — Unusable for production UVM regression.

## Slide 10
SECTION 5
Systematic Elimination → DPI-C Wins
PLI
No C++, no SV types, obsolete, dangerous — cannot work at all
ELIMINATED
FLI
VHDL only. Your entire testbench is SystemVerilog — end of discussion
ELIMINATED
VPI
Wrong tool: designed for database access, not function calls. Insane verbosity for complex C++
ELIMINATED
SystemC
Requires extra license, 2 kernels, massive complexity — overkill for ISA-level model
ELIMINATED
IPC
High latency, sync complexity, no random-stimulus integration
ELIMINATED
File-Based
Cannot work with constrained-random UVM; post-mortem only, loses fine-grained comparison
ELIMINATED
DPI-C
IEEE standard, zero overhead, type-safe, dynamic, UVM-native, simple integration
SELECTED ✓

## Slide 11
SECTION 6
DPI-C: A Direct ABI Contract — Not a Bridge, Not a Translator
DPI-C (Direct Programming Interface for C) is a standardized ABI (Application Binary Interface) contract between a SystemVerilog simulator and compiled C/C++ code, enabling DIRECT function calls across the SV/C boundary. Both run in the SAME process, SAME address space — no serialization, no IPC.
QuestaSim Process — SINGLE ADDRESS SPACE
SV Simulation Engine
UVM Testbench (SV/UVM)
simx_init(2, 4, 4)
exitcode = simx_run()
Direct CALL
instruction
(~5 ns)
◀ return value
simx_model.so (C++ Code)
SimX Processor / RAM / Arch
int simx_init(...) { ... }
int simx_run() { ... }
DPI-C ABI · IEEE 1800
4 What 'Direct' Means Internally
QuestaSim uses dlopen() to load simx_model.so into its own process. Then dlsym() resolves each function pointer. The compiled SV code calls it as a direct CPU CALL instruction — same as C calling C.
4 Type Mapping
SV types map directly to C types in CPU registers — int→int32_t, longint→int64_t, byte[]→svOpenArrayHandle. No serialization. Passing int 5 from SV literally places integer 5 in a CPU register.
4 Bidirectional: Import & Export
SV can call C (import DPI-C) AND C can call back into SV (export DPI-C). This enables per-instruction callbacks from SimX into the UVM scoreboard.
4 context vs pure Qualifier
pure: fastest, no SV interaction. context: required when C needs to call back into SV via export DPI-C — essential for simx_run() which may invoke SV callbacks.

## Slide 12
SECTION 6
DPI-C: Type Mapping System
KEY: The type mapping is DIRECT memory layout — no serialization, no conversion. int 5 in SV is literally integer 5 in a CPU register when C receives it. For arrays, svOpenArrayHandle gives a direct pointer to array data — ZERO COPY.
SystemVerilog Type
C/C++ Type
Bit Width
Notes
byte
char / int8_t
8
Signed 8-bit — direct memory map
shortint
short / int16_t
16
Signed 16-bit — direct memory map
int
int / int32_t
32
Signed 32-bit — in CPU register
longint
long long / int64_t
64
Signed 64-bit — your addr type!
int unsigned
unsigned int
32
Unsigned 32-bit — for DCR addresses
longint unsigned
unsigned long long
64
Unsigned 64-bit
real
double
64
IEEE 754 double precision
string
const char*
ptr
Null-terminated C string
byte data[]
svOpenArrayHandle
dynamic
Dynamic array — most powerful type! Zero-copy pointer.
chandle
void*
ptr
Opaque pointer for C++ object handles

## Slide 13
SECTION 7
Complete UVM Environment with SimX Golden Model
UVM ENVIRONMENT
AGENT
Sequencer
(generates stimulus)
▼
Driver
(sends to RTL DUT)
▼
Monitor
(observes RTL output)
▶
analysis port
(actual results)
GOLDEN MODEL
(SimX via DPI-C)
simx_init()
simx_run() / simx_step()
simx_read_mem()
→ analysis port
▶
expected
results
DPI-C calls ↕
SimX C++ Core
Processor · RAM · Arch · Core · Warp · Instr
SCOREBOARD
Expected Results
(from SimX)
COMPARE ⬇
Actual Results
(from RTL monitor)
PASS / FAIL
RTL DUT (Vortex GPGPU SystemVerilog)

## Slide 14
SECTION 7
Three UVM Integration Patterns for SimX
Pattern 1
Post-Mortem
Final State Comparison
FLOW
1
Load Program into SimX
2
Run SimX to completion (BLOCKING)
3
Read final memory state via simx_read_mem()
4
Compare with RTL's final state in scoreboard
Best for:
Directed tests with known programs
Comparison: Final state only (memory contents, exit code)
Pattern 2
On-the-Fly Step
Intermediate State Co-Simulation
FLOW
1
Load program, initialize SimX
2
Loop: Step SimX N cycles forward
3
Apply same DCR/stimulus changes to SimX as RTL
4
Compare intermediate states with scoreboard
Best for:
Co-simulation with RTL cycle synchronization
Comparison: Intermediate states, handles dynamic DCR changes
Pattern 3
Commit Callback
Per-Instruction Comparison (Gold Standard)
FLOW
1
SimX calls BACK into UVM via export DPI-C
2
On every committed instruction: warp, PC, rd, value
3
UVM scoreboard receives result IMMEDIATELY
4
Compare per-instruction with RTL commit log
Best for:
Maximum coverage — per-instruction verification
Comparison: Every single instruction commit (most powerful)
Increasing Power & Complexity →
P1
P2
P3 ← Gold Standard

## Slide 15
SECTION 7
SimX Lifecycle Through UVM Phases
1
BUILD PHASE
UVM creates simx_golden_model component. Creates Scoreboard. Connects analysis ports. SimX C++ NOT yet touched.
No DPI calls yet
2
CONNECT PHASE
Analysis ports wired: golden model output → scoreboard expected input. Monitor output → scoreboard actual input. Still no C++ SimX calls.
No DPI calls yet
3
RUN PHASE
MAIN ACTIVITY: simx_init() called. SimX C++ objects created. Load program, configure DCRs. Run to completion OR step with RTL. Send expected transactions to scoreboard.
simx_init() → simx_load_bin() → simx_dcr_write() → simx_run() → simx_read_mem() → ap.write()
4
REPORT PHASE
simx_cleanup() called. SimX C++ objects destroyed. Memory freed. UVM prints PASS/FAIL summary with transaction counts and error details.
simx_cleanup() — delete Processor, RAM, Arch
Critical: SimX C++ objects (Processor, RAM, Arch) persist as global static pointers across ALL DPI calls — they live for the entire duration of run_phase.

## Slide 16
SECTION 8
The Makefile: Build Orchestrator & Compilation Pipeline
ROLE: Compiles ALL SimX C++ objects + simx_dpi.cpp + third-party libraries into a single shared library simx_model.so, then launches QuestaSim with that library loaded. It is the glue that connects the C++ world to the SV/UVM world.
INPUTS (What Goes In)
simx_dpi.cpp
Your DPI bridge file — the adapter between SV and SimX
SimX .obj files
Pre-compiled SimX: processor, core, warp, instr, mem, arch
softfloat.a
Static library: IEEE 754 floating-point ops for F/D extensions
libramulator.so
Dynamic library: DRAM timing model for memory simulation
svdpi.h (QuestaSim)
Header for svOpenArrayHandle and DPI types
VX_config.h / VX_types.h
Shared hardware config: NUM_CORES, NUM_WARPS, DCR addrs
▶
g++
-fPIC
-shared
KEY COMPILER FLAGS
-fPIC -shared
Position-Independent Code → shared library output
-DNUM_CORES=2
-DNUM_WARPS=4
-DNUM_THREADS=4
Architecture defines — MUST match RTL compile flags
-I$(QUESTA)/include
Access to svdpi.h for DPI type definitions
-I$(SIMX_DIR)
-I$(HW_DIR)/rtl
SimX headers + hardware config headers
OUTPUT
simx_model.so
CONTENTS:
├─ simx_init
from simx_dpi.cpp
├─ simx_run
from simx_dpi.cpp
├─ simx_step
from simx_dpi.cpp
├─ simx_read_mem
from simx_dpi.cpp
├─ simx_write_mem
from simx_dpi.cpp
├─ simx_dcr_write
from simx_dpi.cpp
├─ Processor class
from SimX .obj
├─ RAM / Arch
from SimX .obj
QuestaSim launch:
vsim -sv_lib simx_model test_top (QuestaSim does: dlopen → dlsym → builds function pointer table → simulation begins)

## Slide 17
SECTION 8
simx_dpi.cpp: The Bridge Layer in Detail
ROLE: Translates UVM/SV function calls into SimX C++ object method calls. It is the stateful adapter that bridges two worlds — the SV type system and the C++ object model. It maintains global SimX state across all DPI calls.
WORLD 1: UVM / SystemVerilog
WORLD 2: SimX C++
SV types: longint, int, byte[]
svOpenArrayHandle for arrays
Calls functions by name from SV
No concept of C++ classes
C++ classes: Processor, RAM, Arch
C++ types: uint64_t, std::vector
Object-oriented: proc->run()
SimX internal state machine
simx_
dpi.cpp
BRIDGE
→
→
GLOBAL STATE (persists across ALL DPI calls)
static g_processor*
Pointer to SimX Processor object — the GPU execution engine
static g_ram*
Pointer to SimX RAM object — page-based 4KB memory model
static g_arch*
Pointer to Arch config — cores, warps, threads, XLEN
extern "C" { ... } is CRITICAL
Without it, C++ name mangling makes dlsym() return NULL → DPI load fails!
7 EXPOSED DPI FUNCTIONS
simx_init()
Create Processor, RAM, Arch objects
simx_load_bin()
Load .bin kernel file into RAM
simx_write_mem()
Write bytes to SimX RAM (zero-copy via svGetArrayPtr)
simx_read_mem()
Read bytes from SimX RAM (zero-copy)
simx_dcr_write()
Configure Device Control Registers
simx_run()
BLOCKING: Run SimX to program completion
simx_step()
Step SimX N cycles (for on-the-fly pattern)

## Slide 18
SECTION 8
Complete Call Chain: From SV to SimX RAM and Back
WRITE PATH: simx_write_mem(0x80000000, 16, program)
L0 — UVM Test (SV)
Call simx_write_mem() with addr=0x80000000, size=16, and a byte array containing the RISC-V instructions.
▼
L1 — DPI-C ABI
QuestaSim maps: longint→uint64_t (CPU register), int→int (CPU register), byte[]→svOpenArrayHandle (descriptor with data pointer).
▼
L2 — simx_dpi.cpp
svGetArrayPtr(handle) returns a raw pointer directly to SV's array memory. ZERO COPY — no data duplication. Calls g_ram->write(src_ptr, addr, size).
▼
L3 — SimX RAM::write()
Calculates page index (addr / 4096). Allocates 4KB page if not exists. memcpy() 16 bytes into page at correct offset. RISC-V instructions now in SimX RAM.
EXECUTION PATH: simx_run()
L0 — UVM Test (SV)
exitcode = simx_run()
QuestaSim is now PAUSED — SimX takes over the CPU thread until program completes.
▼
L2 — simx_dpi.cpp
Calls g_processor->run() — BLOCKING. No DPI type conversion needed (no arguments). QuestaSim waits.
▼
L3 — SimX Processor::run()
Sets all warps active, PC = startup_addr. Enters fetch-decode-execute loop. Steps all cores until every warp hits ebreak.
▼
L4 — SimX Core::step()
FETCH: RAM::read(PC, 4) → 32-bit instruction. DECODE: Parse opcode/rd/rs/imm. EXECUTE: All active threads in SIMT. COMMIT: Update regs, advance PC. On ebreak → return exit code (x3 value).
KEY INSIGHT: SV array and SimX RAM share the SAME process address space. svGetArrayPtr() returns a direct pointer — one memcpy, no IPC, no serialization.

## Slide 19
SECTION 9
All 7 Methods: Side-by-Side Comparison
Feature
PLI
VPI
FLI
SystemC
IPC
File
DPI-C
IEEE Standard
✕
✓
✕
✓
POSIX
N/A
✓
SV Support
✕
✓
✕
Part
✓
✓
✓
C++ Support
✕
Part
✕
✓
✓
✓
✓
Questa Support
✕
✓
✓
Lic.
✓
✓
✓
VCS Support
✕
✓
✕
✓
✓
✓
✓
Performance
Poor
Poor
Med
Good
Poor
Poor
Excellent
Complexity
V.Hi
High
High
V.Hi
High
Low
Low
UVM Native
✕
✕
✕
✕
✕
Part
✓
Dynamic
✕
✓
✓
✓
✓
✕
✓
Type Safe
✕
✕
✕
✓
Part
N/A
✓
For SimX
✕
✕
✕
⚠
⚠
⚠
✓

## Slide 20
Key Takeaways
①
Golden model = single source of truth. Without it, you cannot detect RTL bugs at GPGPU scale.
②
SimX is the ONLY correct choice for Vortex — it models SIMT, custom instructions, and DCRs that no external tool handles.
③
C++ for golden models is industry standard. DPI-C is IEEE standardized (1800-2005) — not a workaround, not a hack.
④
DPI-C is a direct ABI contract — same process, same memory, ~5 ns overhead. Not a bridge, not a translator.
⑤
Architecture: SV test → simx_dpi.cpp (bridge) → SimX C++ objects. Three patterns: Post-Mortem → On-the-Fly → Commit Callback.
⑥
Makefile: g++ -fPIC -shared produces simx_model.so. QuestaSim: vsim -sv_lib simx_model. Two files, one shared library, zero IPC.
VERIFICATION ARCHITECTURE STACK
UVM Testbench (SV/UVM)
DPI-C ABI Layer (IEEE 1800)
simx_dpi.cpp (Bridge)
SimX C++ Core
Hardware Config (VX_config.h)
Vortex GPGPU Verification Team · Golden Model Implementation · 2025