## Slide 1
GPGPU
SimX Golden Model
& DPI-C Integration
for Vortex GPGPU UVM Verification
Team: Vortex UVM Verification
Tool: QuestaSim 2021 | Platform: Ubuntu 22.04
Language: SystemVerilog + C++ (DPI-C)

## Slide 2
What We'll Cover
01
Golden Model Options
Why SimX over Spike, POCL, Verilator
02
C++ for Golden Models
Industry standard — ARM, Intel, NVIDIA do it too
03
Integration Methods
All 7 ways to bridge C++ ↔ SV/UVM
04
What is DPI-C?
Not a translator — a direct binary bridge
05
DPI-C in UVM Flow
How SimX lives inside the UVM environment
06
File Deep-Dive
simx_dpi.cpp · simx_pkg.sv · Makefile

## Slide 3
Golden Model Options for Vortex
Which simulators could serve as golden reference?
A Spike
RISC-V ISA Simulator
Official RISC-V Foundation reference
✗ No GPU warps/threads model
✗ No Vortex ISA extensions
✗ No DCR registers
B POCL
Portable Computing Language
Runs same OpenCL kernels on CPU
✗ Algorithm-level only
✗ No microarchitecture model
✗ No memory hierarchy
C Verilator
RTL at Higher Speed
Fast RTL simulation
✗✗ RTL vs itself — useless!
✗✗ Defeats verification purpose
Dangerous false confidence
D SimX
Vortex Functional Simulator
⭐ BEST CHOICE
✓ Models every warp & thread
✓ Full Vortex ISA extensions
✓ DCRs + memory hierarchy
✓ Same team, used in CI
SimX is located at: sim/simx/ — written by the Vortex team, used in their own CI pipeline to validate the RTL

## Slide 4
Why SimX is the Definitive Choice
Criterion | SimX ✓ | Spike | POCL | Verilator
Models Vortex Warps/Threads | ✓ Exactly | ✗ No | ✗ No | ✗ Partial
Vortex ISA Extensions | ✓ Exactly | ✗ No | ✗ No | ✗ Partial
Memory Hierarchy (Cache+DRAM) | ✓ Full | ✗ Flat | ✗ OS | ✓ RTL only
DCR Register Model | ✓ Yes | ✗ No | ✗ No | ✓ RTL only
Shared Memory / Barriers | ✓ Yes | ✗ No | ≈ Approx | ✓ RTL only
Written by Vortex Team | ✓ Yes | ✗ No | ✗ No | ✗ No
Used in Vortex CI Pipeline | ✓ Yes | ✗ No | ✗ No | ✗ No
Same Memory Map (0x80000000) | ✓ Exact | ✗ No | ✗ No | ≈ Depends

## Slide 5
Is C++ Normal for Golden Models?
YES — it is the industry standard approach
Why C++ Dominates
⚡
Speed
100x–1000x faster than RTL sim — results in microseconds
🔷
Abstraction Level
Models WHAT happens, not HOW — behavioral, not structural
⚙️
Algorithm-Friendly
C++ STL: file I/O, exceptions, FP math, containers
🚫
SV is Wrong Tool
Only use SV golden model for trivial blocks (FIFO, regfile)
Industry Precedent
ARM
Fast Models
C++ Cycle Models for Cortex verification
Intel
SoftSIM
C++ ISS for Core processor validation
NVIDIA
Functional Sim
C++ GPU shader behavior reference
RISC-V
Spike
C++ ISA reference — the community standard
Vortex
SimX
C++ GPGPU ISA simulator — your golden model

## Slide 6
All Ways to Integrate C++ with SV/UVM
1
DPI-C
✓ CHOSEN
+ IEEE std · Zero overhead · In-process · Bidirectional
- Type mapping needed · .so must be -fPIC
2
PLI/VPI
LEGACY
+ Works with any old simulator · Can introspect hierarchy
- Verbose C API · Deprecated · Slow · Nobody uses it now
3
SystemC + TLM-2.0
VIABLE
+ Clean OOP model · QuestaSim native · TLM-2.0 standard
- SimX isn't SystemC — needs sc_module wrap · Overhead
4
IPC (Sockets/Pipes)
OVERKILL
+ Full isolation · Multi-machine possible
- High latency · Serialization · Sync complexity
5
File Exchange
SIMPLE
+ Zero complexity · Any tool works
- Post-mortem only · No live feedback · Slow for big mem
6
e/Specman (HVL)
DEAD
+ Was industry std in 2000s
- Proprietary · Cadence only · Replaced by UVM+DPI
7
MATLAB/Simulink
WRONG
+ Great for DSP/signal work
- Extreme cost · Cannot model RISC-V ISA semantics

## Slide 7
What is DPI-C? — The Core Concept
❌ DPI-C is NOT: a translator · a compiler · a language wrapper (SWIG/ctypes) · a process boundary · a code generator
✓ DPI-C IS: A direct binary interface bridge — a standardized calling convention for the SV simulator to call compiled C/C++ functions in a shared library (.so), in the same process, at near-zero cost.
SV
SV Code
import "DPI-C"
function simx_init()
►
↔
DPI Runtime
dlopen / dlsym
arg marshaling
►
C+
C++ Function
extern "C"
simx_init() { ... }
extern "C"
Disables C++ name mangling → plain symbol names in .so
svdpi.h
Provides svOpenArrayHandle, svBitVecVal — the interface types
-sv_lib simx_model
Tells vsim to dlopen() the .so before simulation starts
import "DPI-C"
Declares the function prototype — SV compiler trusts the .so

## Slide 8
DPI-C Architecture: Inside QuestaSim Process
QuestaSim vsim — Single OS Process (Everything here shares the same memory space)
SV Simulator Kernel
UVM Testbench
import "DPI-C"
simx_init(2,4,4)
simx_write_mem(..)
simx_run()
simx_read_mem(..)
ap.write(txn)
▶
DPI-C Runtime
dlopen('simx_model.so')
dlsym('simx_init')
─────────────────
SV int → C int
SV string→ char*
SV byte[]→ svHandle
─────────────────
Jump to C++
▶
simx_model.so
simx_init() {}
g_processor*
g_ram* (4 GB)
g_arch*
─────────────
softfloat.a
libramulator
SimX .obj files
KEY INSIGHT: Zero-copy | Same process memory | No serialization | No IPC overhead

## Slide 9
UVM Environment Architecture
UVM Environment
Vortex Agent
Vortex Agent
Sequencer
Driver
Monitor
actual TXN ►
Scoreboard
actual ← from RTL
expected ← from SimX
────────────────
actual ≟ expected
✓ PASS / ✗ FAIL
expected TXN ▲
simx_golden_model (UVM Component — run_phase)
simx_init()
→
simx_load_bin()
→
simx_write_mem()
→
simx_dcr_write()
→
simx_run()
→
simx_read_mem()
→
ap.write(txn)

## Slide 10
Complete Write/Read Data Flow — Vector Addition Example
1
simx_init()
SV: cfg.num_cores, warps, threads
C++: new Arch() · new RAM(4GB) · new Processor()
attach_ram(g_ram)
2
simx_load_bin()
SV: cfg.kernel_path, 64'h80000000
C++: g_ram->write(kernel bytes, 0x80000000)
3
simx_write_mem()
SV: byte input_A[]
→ 64'h90000000
C++: svGetArrayPtr(data) → g_ram->write(src, addr)
4
simx_dcr_write()
SV: STARTUP_ADDR · NUM_THREADS
C++: g_processor->dcr_write(addr, val)
5
simx_run()
SV: ret = simx_run()
C++: g_processor->run() — all warps, all instrs
g_ram[0x90020000] = [results]
6
simx_read_mem()
SV: result_data = new[cfg.data_size]
C++: g_ram->read(dest, 0x90020000) — ZERO COPY
7
ap.write(txn)
SV: expected_txn → Scoreboard
C++: → Scoreboard.write_golden() → compare vs RTL

## Slide 11
File Deep-Dive: simx_dpi.cpp
The Bridge Layer — Most Critical File
1 · Global State Ownership
static Processor* g_processor = nullptr;
static RAM* g_ram = nullptr;
static Arch* g_arch = nullptr;
These statics live in .so's data segment — persist between ALL DPI calls.
This is how SimX remembers its state between init/run/read.
2 · extern "C" Block
extern "C" {
int simx_init(...) { ... }
void simx_run() { ... }
}
Disables C++ name mangling. Without this, 'simx_init' becomes
'_Z10simx_initiii' — SV import declarations cannot find it.
3 · Zero-Copy Data Bridge
uint8_t* src = (uint8_t*)svGetArrayPtr(data);
g_ram->write(src, addr, size);
svOpenArrayHandle is an opaque handle to a SV dynamic array.
svGetArrayPtr() returns raw C pointer — same physical memory.
No copying. No serialization. They literally share bytes.
4 · Bootstrap (x3 Register Init)
uint8_t bootstrap[16] = {
0x93,0x01,0x00,0x00, // addi x3,x0,0
0x97,0x00,0x00,0x00, // auipc x1,0
0x67,0x80,0x00,0x01 // jalr x0,x1,16
}
SimX uses x3 as exit code reg but RISC-V startup doesn't init it.
Bootstrap injects 3 instructions at 0x80000000-16, sets x3=0,
then jumps to real entry point. Elegant low-level fix.

## Slide 12
File Deep-Dive: simx_pkg.sv + Makefile
simx_pkg.sv — SV-Side Interface
Purpose 1 – DPI-C Declarations
import "DPI-C" context function int simx_init(...);
Tells SV compiler: "this function lives in a .so"
Resolved at link time when vsim loads the library
Purpose 2 – UVM Component Class
simx_golden_model extends uvm_component
Wraps all DPI calls inside proper UVM phases:
build_phase → run_phase → report_phase
⚠ Mismatch to Fix (Critical!)
sv declares: simx_init(string kernel_file, int...)
cpp implements: simx_init(int cores, warps, threads)
→ Fix: align signatures or add kernel_file to C++
Makefile — Build Orchestrator
The Core Build Command
g++ simx_dpi.cpp $(SIMX_OBJS) softfloat.a
-lramulator -fPIC -shared → simx_model.so
Links pre-built SimX .o files — don't recompile
-D Defines MUST Match RTL Config
-DNUM_CORES=2 -DNUM_WARPS=4 -DNUM_THREADS=4
SimX reads these at COMPILE TIME for Arch()
Mismatch = wrong model = false failures
-Wl,-rpath (Runtime Library Path)
Embeds Ramulator search path into the .so
vsim finds libramulator.so without manual
export LD_LIBRARY_PATH before every run
-sv_lib simx_model (vsim flag)
Tells QuestaSim: dlopen('simx_model.so')
before any SV code executes.
This is what makes import "DPI-C" work.

## Slide 13
Critical Issues to Fix Before Moving Forward
01
CRITICAL — Linker Error
simx_init() Signature Mismatch
Problem: simx_pkg.sv declares: simx_init(string kernel_file, int cores, warps, threads)
simx_dpi.cpp exports: simx_init(int cores, warps, threads)
→ vsim will fail at runtime: unresolved DPI import
Fix: Option A: Remove kernel_file from SV declaration, call simx_load_bin() separately
Option B: Add 'const char* kernel_file' param to the C++ simx_init() body
02
BUG — Wrong Execution Mode
Missing simx_run() Import in simx_pkg.sv
Problem: pkg calls void'(simx_step(0)) as run workaround
simx_step() advances N cycles — passing 0 does nothing!
simx_run() exists in C++ but is never declared/called in SV
Fix: Add: import "DPI-C" context function int simx_run();
Call ret = simx_run(); in run_phase instead of simx_step(0)
03
IMPORTANT — Config Sync
Makefile -D Defines Must Mirror RTL Config
Problem: -DNUM_CORES=2 -DNUM_WARPS=4 -DNUM_THREADS=4 in Makefile
must exactly match values in vortex_config.sv at all times
If RTL changes config but Makefile is not updated → false mismatches
Fix: Create a shared config header or a build variable that feeds both.
Consider generating Makefile defines from vortex_config.sv at build time.

## Slide 14
Key Takeaways
🏆
SimX is the ONLY correct golden model — it's the same reference the Vortex team uses in CI
⚡
C++ golden models are industry standard (ARM, Intel, NVIDIA) — 100–1000× faster than SV
🔗
DPI-C is a direct binary bridge — not a translator. Same process, same memory, zero overhead
🔧
simx_dpi.cpp owns the C++ state; svdpi.h bridges types; Makefile links it all into simx_model.so
🔄
The flow is: init → load_bin → write_mem → dcr_write → run → read_mem → scoreboard compare
⚠️
Fix 3 issues NOW: align simx_init() signatures, add simx_run() import, sync Makefile defines
Vortex UVM Verification Team · Golden Model: SimX + DPI-C · QuestaSim 2021 / Ubuntu 22.04