## Slide 1
GPGPU
SimX Golden Model
& DPI-C Integration
Complete Deep Guide — Project Files, Architecture & Full Example
Team: Vortex UVM Verification
Tool: QuestaSim 2021 | Platform: Ubuntu 22.04
Version 2 — File Deep-Dive & Complete Example Walkthrough

## Slide 2
What We'll Cover
01
Golden Model Options
SimX vs Spike, POCL, Verilator
02
Why C++ for Golden Models
Industry standard — ARM, Intel, NVIDIA
03
All Integration Methods
7 ways — why DPI-C wins
04
What is DPI-C?
Binary bridge, not translator
05
Deep File Dives
simx_dpi.cpp · simx_pkg.sv · vortex_config.sv · Makefile · test_top.sv
06
Complete Example
UVM call → DPI bridge → SimX runs → results return to UVM

## Slide 3
Golden Model Options for Vortex
Which simulators could serve as golden reference?
A Spike
RISC-V ISA Simulator
Official RISC-V Foundation reference
✗ No GPU warps/threads model
✗ No Vortex ISA extensions
✗ No DCR registers
B POCL
Portable Computing Language
Runs same OpenCL kernels on CPU
✗ Algorithm-level only
✗ No microarchitecture
✗ No memory hierarchy
C Verilator
RTL at Higher Speed
Fast RTL simulation
✗✗ RTL vs itself — useless!
✗✗ Defeats verification purpose
Dangerous false confidence
D SimX
Vortex Functional Simulator
⭐ BEST CHOICE
✓ Models every warp & thread
✓ Full Vortex ISA extensions
✓ DCRs + memory hierarchy
✓ Same team, used in CI
SimX lives at: sim/simx/ — Written by the Vortex team, used in their own CI pipeline to validate the RTL

## Slide 4
Why SimX is the Definitive Choice
Criterion | SimX ✓ | Spike | POCL | Verilator
Models Vortex Warps/Threads | ✓ Exactly | ✗ No | ✗ No | ✗ Partial
Vortex ISA Extensions | ✓ Exactly | ✗ No | ✗ No | ✗ Partial
Memory Hierarchy (Cache+DRAM) | ✓ Full | ✗ Flat | ✗ OS | ✓ RTL only
DCR Register Model | ✓ Yes | ✗ No | ✗ No | ✓ RTL only
Shared Memory / Barriers | ✓ Yes | ✗ No | ≈ Approx | ✓ RTL only
Written by Vortex Team | ✓ Yes | ✗ No | ✗ No | ✗ No
Used in Vortex CI Pipeline | ✓ Yes | ✗ No | ✗ No | ✗ No
Same Memory Map (0x80000000) | ✓ Exact | ✗ No | ✗ No | ≈ Depends

## Slide 5
Is C++ Normal for Golden Models?
YES — it is the industry standard approach
Why C++ Dominates
⚡
Speed
100x–1000x faster than RTL sim — results in microseconds, not hours
🔷
Abstraction Level
Models WHAT happens, not HOW — behavioral, not structural
⚙️
Algorithm-Friendly
C++ STL: file I/O, exceptions, FP math, containers, all native
🚫
SV is Wrong Tool
Only use SV golden model for trivial blocks (FIFO, regfile)
Industry Precedent
ARM
Fast Models
C++ Cycle Models for Cortex verification
Intel
SoftSIM
C++ ISS for Core processor validation
NVIDIA
Functional Sim
C++ GPU shader behavior reference
RISC-V
Spike
C++ ISA reference — the community standard
Vortex
SimX
C++ GPGPU ISA simulator — your golden model

## Slide 6
All Ways to Integrate C++ with SV/UVM
1
DPI-C
✓ CHOSEN
+ IEEE std · Zero overhead · In-process · Bidirectional
- Type mapping needed · .so must be -fPIC
2
PLI/VPI
LEGACY
+ Works with old simulators · Can introspect hierarchy
- Verbose API · Deprecated · Slow · Nobody uses
3
SystemC+TLM-2.0
VIABLE
+ Clean OOP · QuestaSim native · TLM-2.0 standard
- SimX isn't SystemC — extra wrap overhead
4
IPC (Sockets/Pipes)
OVERKILL
+ Full isolation · Multi-machine possible
- High latency · Serialization · Sync complexity
5
File Exchange
SIMPLE
+ Zero complexity · Any tool works
- Post-mortem only · No live feedback · Slow
6
e/Specman (HVL)
DEAD
+ Was industry std in 2000s
- Proprietary · Cadence only · Replaced by UVM
7
MATLAB/Simulink
WRONG
+ Great for DSP/signal work
- Extreme cost · Cannot model RISC-V ISA

## Slide 7
What is DPI-C? — The Core Concept
❌ DPI-C is NOT: a translator · a compiler · a language wrapper (SWIG/ctypes) · a process boundary · a code generator
✓ DPI-C IS: A direct binary interface bridge — standardized calling convention for SV simulator to call compiled C/C++ in a shared library, in the same process, at near-zero cost.
SV
SV Code
import "DPI-C"
function simx_init()
►
↔
DPI Runtime
dlopen / dlsym
arg marshaling
►
C+
C++ Function
extern "C"
simx_init() { ... }
extern "C"
Disables C++ name mangling → plain symbol names visible in .so
svdpi.h
Provides svOpenArrayHandle, svBitVecVal — the interface types
-sv_lib simx_model
Tells vsim to dlopen() the .so before simulation starts
import "DPI-C"
Declares the function prototype — SV compiler trusts the .so

## Slide 8
DPI-C Architecture: Inside QuestaSim Process
QuestaSim vsim — Single OS Process (Everything shares the same memory space — zero-copy, zero-overhead)
SV Simulator Kernel
UVM Testbench
import "DPI-C"
simx_init(2,4,4)
simx_write_mem(..)
simx_run()
simx_read_mem(..)
ap.write(txn)
▶
DPI-C Runtime
dlopen('simx_model.so')
dlsym('simx_init')
─────────────────
SV int → C int
SV string→ char*
SV byte[]→ svHandle
─────────────────
Jump to C++
▶
simx_model.so
simx_init() {}
g_processor*
g_ram* (4 GB)
g_arch*
─────────────
softfloat.a
libramulator
SimX .obj files
KEY: Zero-copy | Same process memory | No serialization | No IPC overhead | g_processor/g_ram persist between all DPI calls

## Slide 9
UVM Environment Architecture
UVM Environment
Vortex Agent
Sequencer
Driver
Monitor
actual TXN ►
Scoreboard
actual ← from RTL
expected ← from SimX
────────────────
actual ≟ expected
✓ PASS / ✗ FAIL
expected TXN ▲
simx_golden_model (UVM Component — run_phase)
simx_init()
→
simx_load_bin()
→
simx_write_mem()
→
simx_dcr_write()
→
simx_run()
→
simx_read_mem()
→
ap.write(txn)

## Slide 10
7-Phase Data Flow — Vector Addition Example
1
simx_init()
SV: cfg.num_cores, warps, threads
C++: new Arch() · new RAM(4GB) · new Processor()
attach_ram(g_ram), verify RAM
2
simx_load_bin()
SV: cfg.kernel_path, 64'h80000000
C++: g_ram->write(kernel bytes, 0x80000000)
3
simx_write_mem()
SV: byte input_A[] → 64'h90000000
C++: svGetArrayPtr(data) → g_ram->write(src,addr)
4
simx_dcr_write()
SV: STARTUP_ADDR · NUM_THREADS
C++: g_processor->dcr_write(addr, val)
5
simx_run()
SV: exitcode = simx_run()
C++: g_processor->run() — all warps, all instrs
g_ram[0x90020000] = [results]
6
simx_read_mem()
SV: result_data = new[cfg.data_size]
C++: g_ram->read(dest, 0x90020000) — ZERO COPY
7
ap.write(txn)
SV: expected_txn → Scoreboard
C++: → Scoreboard.write_golden() → compare vs RTL

## Slide 11
Project Files
Deep Dive — What Each File IS and What It Does
simx_dpi.cpp
simx_pkg.sv
vortex_config.sv
Makefile
test_top.sv

## Slide 12
simx_dpi.cpp — Part 1: What It Is & Global State
What is this file?
The bridge layer. simx_dpi.cpp is the ONLY file that has access to both worlds simultaneously — it sees SystemVerilog arrays (via svdpi.h) and it owns the SimX C++ objects (Processor, RAM, Arch). Nothing else touches both. It compiles into simx_model.so — the shared library loaded by QuestaSim at startup.
File structure (435 lines)
▸ #includes + using namespace vortex
svdpi.h, processor.h, arch.h, mem.h, VX_config.h
▸ Static globals (6 pointers/flags)
g_processor, g_ram, g_arch, g_initialized, g_startup_addr, g_ram_attached
▸ extern "C" { ... }
7 exported functions: cleanup, init, init_exit_code, load_bin, write_mem, read_mem, dcr_write, run, step
Section 1 — Global State: Why statics?
// These 6 statics live in the .so's
// BSS/data segment. They PERSIST
// between every single DPI call.
static Processor* g_processor = nullptr;
static RAM* g_ram = nullptr;
static Arch* g_arch = nullptr;
Why static globals and NOT local variables?
✓ When SV calls simx_init() → objects created in .so memory
✓ When SV calls simx_write_mem() → same g_ram still exists
✓ When SV calls simx_run() → same g_processor executes
✓ When SV calls simx_read_mem() → same g_ram has results
✗ Local vars would die at end of each function call ← WRONG!
Section 2 — simx_init(): What it actually does
int simx_init(int nc, int nw, int nt) {
g_arch = new Arch(nt, nw, nc); // ORDER: threads,warps,cores!
g_ram = new RAM(0x100000000ULL, 4096); // 4GB, 4KB pages
g_processor = new Processor(*g_arch);
g_processor->attach_ram(g_ram); // processor can see RAM
// verify: write 0xDEADBEEF, read back, check match

## Slide 13
simx_dpi.cpp — Part 2: Memory & Execution Functions
simx_write_mem() — How SV byte[] becomes uint8_t* in C++ WITHOUT copying
void simx_write_mem(uint64_t addr, int size,
const svOpenArrayHandle data) {
// svGetArrayPtr: gets RAW pointer into SV array's memory
uint8_t* src = (uint8_t*)svGetArrayPtr(data);
g_ram->write(src, addr, size); // direct, zero-copy
}
Key: svOpenArrayHandle
An opaque handle to a SV dynamic array (byte data[]).
svGetArrayPtr() returns a raw C pointer to the same physical bytes — the SV simulator and C++ literally share the same memory addresses.
No memcpy. No buffer. Zero overhead.
simx_read_mem() — How results in g_ram get back to SV byte array after execution
void simx_read_mem(uint64_t addr, int size,
const svOpenArrayHandle data) {
uint8_t* dest = (uint8_t*)svGetArrayPtr(data);
g_ram->read(dest, addr, size); // reads from SimX RAM
} // dest IS the SV byte[], same memory, no copy
After simx_run() returns:
g_ram contains the FULL state of memory after every warp executed every instruction. Calling read_mem() at the result address gives you exactly what the GPU program wrote.
simx_run() — Run to completion
int simx_run() {
int exitcode = g_processor->run(); // blocking
return exitcode; // 0 = success
simx_dcr_write() — Configure the processor
void simx_dcr_write(uint32_t addr, uint32_t value) {
g_processor->dcr_write(addr, value);
} // Sets STARTUP_ADDR, NUM_THREADS, etc.

## Slide 14
simx_dpi.cpp — Part 3: Bootstrap (x3 Register Problem)
The Problem
SimX's Processor::run() uses register x3 as the exit code register. When the RISC-V program finishes (ebreak), run() reads x3 and returns it as the exit code. BUT — x3 is NOT initialized by the RISC-V startup convention (the ABI only guarantees x0=0). So x3 could contain any garbage value like 0x4D414C4C ('MALL') causing run() to return a false failure exit code even when the program ran correctly.
The Fix — simx_init_exit_code_register(): inject 3 RISC-V instructions at startup_addr - 16
// Bootstrap code written to RAM at (startup_addr - 16)
uint8_t bootstrap[16] = {
// Instruction 1: addi x3, x0, 0 (set x3 = 0)
0x93, 0x01, 0x00, 0x00, // → x3 = 0 (exit code)
// Instruction 2: auipc x1, 0 (get current PC)
0x97, 0x00, 0x00, 0x00, // → x1 = bootstrap_addr
// Instruction 3: jalr x0, x1, 16 (jump to x1+16)
0x67, 0x80, 0x00, 0x01 // → jumps to startup_addr
};
Memory Layout After Bootstrap Install
0x7FFFFFF0
addi x3,x0,0
0x7FFFFFF4
auipc x1, 0
0x7FFFFFF8
jalr x0, x1, 16
0x7FFFFFFC
nop (padding)
0x80000000
← real program starts
After writing bootstrap to RAM, the function also updates the DCR STARTUP_ADDR to point to the bootstrap address (0x7FFFFFF0), so the processor fetches from there first. It sets x3=0, then jumps to the real program at 0x80000000. Elegant — zero changes to user program needed.

## Slide 15
simx_pkg.sv — The SV-Side Interface Package
Role: simx_pkg.sv is the SystemVerilog "declaration layer". It tells the SV compiler that certain functions exist in a compiled .so file, without needing to know how they work. It also wraps those calls in a proper UVM component class (simx_golden_model) with lifecycle phases.
Part 1 — DPI-C import declarations (the bridge declarations)
import "DPI-C" context function int simx_init(
input string kernel_file, // ⚠ MISMATCH! Not in cpp
input int num_cores,
input int num_warps,
input int num_threads);
import "DPI-C" context function int simx_step(
input int cycles); // ⚠ BUG: simx_run() not imported!
⚠ 2 Critical Mismatches
1. simx_init() signature:
SV has 'string kernel_file'
C++ has NO such param
→ Linker error at runtime!
2. simx_run() missing:
SV calls simx_step(0)
But step(0) = noop!
Needs import of simx_run()
Part 2 — simx_golden_model class structure (UVM component)
class simx_golden_model extends uvm_component;
vortex_config cfg; // gets cfg in build_phase
uvm_analysis_port #(uvm_sequence_item) ap; // sends expected txn to scoreboard
task run_phase(phase): simx_init→write_mem→dcr_write→run→read_mem→ap.write
function report_phase(phase): simx_cleanup(); // CRITICAL — free C++ objects
endclass

## Slide 16
vortex_config.sv — The Central Config Object
This file is the Single Source of Truth. EVERY component reads from it — driver, golden model, scoreboard, assertions all pull from the same cfg object stored in uvm_config_db.
Architecture
num_clusters, num_cores, num_warps, num_threads
num_barriers = num_warps / 2
socket_size, issue_width, ibuf_size
ISA Extensions
xlen_64, xlen (32 or 64)
ext_f, ext_d, ext_m, ext_a, ext_c, ext_zicond
flen (0, 32, or 64)
Cache Hierarchy
icache_enable/size, dcache_enable/size
l2_enable/size, l3_enable/size
cache_line_size, num_icaches, num_dcaches
Test/SimX
simx_enable — gate the golden model
program_path, result_base_addr
result_size_bytes, simx_timeout_cycles
Memory Map
startup_addr = 0x80000000 (default)
stack_base_addr = startup + 1MB
io_base_addr = 0xFF000000
Key insight: set_defaults_from_vx_config() reads Makefile -D defines (NUM_CORES, NUM_WARPS...) via `ifdef — config and Makefile must match at ALL times

## Slide 17
Makefile — Build Orchestrator
The Makefile's job: compile simx_dpi.cpp + link pre-built SimX objects + link dependencies → produce simx_model.so
The Core Build Line — everything that goes into simx_model.so
$(CXX) -shared -fPIC \
-I$(QUESTA_HOME)/include \ # for svdpi.h
-I$(SIMX_DIR) -I$(HW_DIR) \ # for processor.h, arch.h, VX_config.h
simx_dpi.cpp $(SIMX_OBJS) softfloat.a -lramulator \
-Wl,-rpath,$(RAMULATOR_LIB_DIR) -o simx_model.so
-shared -fPIC
Tells linker to produce a shared library (.so) instead of executable. -fPIC = Position Independent Code — required for any code that can be dlopen()'d by vsim at any load address.
$(SIMX_OBJS)
Pre-compiled SimX .o files: processor.o, core.o, warp.o, instr.o, etc. You run 'make' in sim/simx/ first, then link those objects HERE instead of recompiling them. This avoids duplicating SimX's build system.
-DNUM_CORES=2 -DNUM_WARPS=4
Architecture defines that SimX reads at COMPILE TIME. The Arch() constructor uses NUM_THREADS, NUM_WARPS, NUM_CORES constants. If these don't match the RTL's VX_config.vh, SimX models a different processor → false failures.
-Wl,-rpath
Embeds Ramulator library path inside the .so itself. Without this, vsim can't find libramulator.so at runtime unless LD_LIBRARY_PATH is manually set before every simulation run.
vsim invocation: vsim -c -sv_lib simx_model → 'simx_model' tells vsim to dlopen simx_model.so before any SV code runs

## Slide 18
test_top.sv — The Actual Test Module
test_top.sv is the standalone SV test module that wires up DPI-C imports and calls them in a structured sequence. This is where you see exactly how the functions are called in practice.
DPI declarations at module level (top of test_top.sv)
import "DPI-C" context function int simx_init(int nc, int nw, int nt);
import "DPI-C" context function void simx_write_mem(longint, int, input byte data[]);
import "DPI-C" context function void simx_read_mem(longint, int, inout byte data[]);
import "DPI-C" context function int simx_run();
import "DPI-C" context function void simx_dcr_write(int addr, int value);
import "DPI-C" context function void simx_init_exit_code_register();
Note: test_top.sv uses the CORRECT simx_init() signature — no kernel_file param. This is the reference for fixing simx_pkg.sv.
Also imports simx_run() properly (not simx_step).
Execution sequence in initial begin block:
1
simx_init(num_cores, num_warps, num_threads)
Creates all C++ objects, verifies RAM with 0xDEADBEEF test
2
configure_dcrs()
Calls simx_dcr_write(VX_DCR_BASE_STARTUP_ADDR0, startup_addr[31:0])
3
load_test_program(startup_addr)
Builds byte[] with RISC-V instructions, calls simx_write_mem()
4
simx_init_exit_code_register()
Optional: installs bootstrap at startup-16, updates DCR
5
exitcode = simx_run()
Blocks until all warps finish — fast: microseconds for short kernels
6
check_results(result_addr, result_size)
Calls simx_read_mem(), reads result bytes, checks against expected

## Slide 19
Complete Example
UVM Test → DPI Bridge → SimX Executes → Results Return to UVM
We trace a single call — simx_write_mem() — through all 4 layers showing exactly what code runs and where
Layer 1: UVM Test (SV)
Layer 2: DPI-C Bridge
Layer 3: SimX C++ Execution
Layer 4: Results Return to UVM

## Slide 20
Layer 1 — UVM Test Calls the Function (SV Side)
Scenario: You have a vector-addition kernel. You need to write array A (input data) into SimX memory. Here is what happens — line by line — when the UVM run_phase calls simx_write_mem().
simx_golden_model::run_phase() in simx_pkg.sv
← This is where you write the call
task run_phase(uvm_phase phase);
// ── STEP 1: declare a SV dynamic byte array
byte input_A[];
input_A = new[cfg.data_size]; // allocate e.g. 1024 bytes in SV heap
// ── STEP 2: fill it with stimulus (from config or sequence)
foreach(input_A[i]) input_A[i] = cfg.input_A[i];
// ── STEP 3: call the DPI-C function ← this is the magic line
simx_write_mem( // function declared via import DPI-C
64'h90000000, // address in SimX's 4GB RAM
cfg.data_size, // number of bytes to write
input_A // the byte array — SV passes handle
);
What SV actually does: It builds the function call on the SV call stack and invokes the DPI-C dispatch mechanism. The SV simulator does NOT jump anywhere yet — it just packages the arguments and hands them to the DPI-C runtime layer. The 3rd argument (input_A) is passed as an svOpenArrayHandle — an opaque descriptor of where the array lives in SV memory.

## Slide 21
Layer 2 — DPI-C Bridge Hands Off to C++
The DPI-C runtime (inside QuestaSim) performs argument marshaling and jumps into simx_model.so. This is invisible to you but critical to understand.
Step A: Resolve symbol
vsim already ran dlopen('simx_model.so')
at startup (via -sv_lib simx_model)
simx_write_mem symbol was resolved then
Now dlsym() lookup is instant — cached
// vsim startup pseudocode:
void* lib = dlopen('simx_model.so');
sym = dlsym(lib, 'simx_write_mem');
// done — sym points to C++ function
Step B: Marshal arguments
SV int → C int (direct register copy)
SV longint → uint64_t (direct)
SV byte[] → svOpenArrayHandle
(opaque descriptor, NOT a copy)
// DPI runtime marshaling:
uint64_t c_addr = sv_longint_val(arg0);
int c_size = sv_int_val(arg1);
svHandle c_data = sv_array_handle(arg2);
Step C: Jump to C++ function
CPU instruction pointer jumps to
the compiled C++ code in .so
NO process switch — same thread
same stack — microsecond cost
// What CPU sees:
// call [sym] ← direct function call
// simx_write_mem(addr, size, handle)
// now executing C++ code

## Slide 22
Layer 3 — SimX C++ Function Executes
Now execution is inside simx_dpi.cpp. Real C++ code runs. Here is the complete annotated body of simx_write_mem() with every line explained.
void simx_write_mem(uint64_t addr, int size,
const svOpenArrayHandle data) {
// Guard: if init() wasn't called first, abort
if (!g_initialized || !g_ram) return;
// Get raw pointer to SV array's memory
uint8_t* src = (uint8_t*)svGetArrayPtr(data);
if (!src) return; // null check
// Write directly to SimX RAM (zero-copy)
g_ram->write(src, addr, size);
// Debug output (visible in vsim console)
cout << "[SimX-DPI] Wrote " << size
<< " bytes to 0x" << hex << addr;
}
Guard clause — all functions check g_initialized first. If UVM forgot to call simx_init(), this returns safely with an error log instead of segfaulting.
svGetArrayPtr(data) is the DPI-C standard API call that extracts the raw C pointer from the SV array handle. After this line, src points to the SAME bytes as input_A[] in SV. No memcpy happened.
g_ram->write() is SimX's RAM class write method. src is a C pointer into SV memory, addr is 0x90000000, size is 1024. The bytes from the SV array land directly in g_ram's page table.
The cout debug output is printed to the vsim console. You can see '[SimX-DPI] Wrote 1024 bytes to 0x90000000' followed by the first bytes — very useful for debugging.

## Slide 23
Layer 3b — Inside simx_run(): What SimX Actually Does
After all write_mem and dcr_write calls are done, the UVM golden model calls simx_run(). This is the most important call — it triggers real RISC-V execution inside SimX.
int simx_run() {
// g_processor->run() is BLOCKING
// it doesn't return until the kernel finishes
int exitcode = g_processor->run();
return exitcode; // 0 = success
}
What g_processor->run() does inside SimX:
→ Fetches first instruction from g_ram[startup_addr]
→ Decodes it as RISC-V (supports Vortex GPU extensions)
→ Executes it across all warps × all threads
→ Advances PC, handles branches, loops, memory ops
→ Repeats until ebreak or exit system call
→ Reads x3 register → returns as exit code
Memory state before / during / after simx_run()
BEFORE run()
0x80000000
kernel binary
[RISC-V instructions, loaded by load_bin()]
0x90000000
input_A
[1,2,3,4,...] — written by simx_write_mem()
0x90010000
input_B
[10,20,30,40,...] — written by simx_write_mem()
0x90020000
output_C
[??] — not yet written
AFTER run()
0x80000000
kernel binary
[unchanged]
0x90000000
input_A
[1,2,3,4,...] — unchanged
0x90010000
input_B
[10,20,30,40,...] — unchanged
0x90020000
output_C
[11,22,33,44,...] ← written by GPU kernel!

## Slide 24
Layer 4 — Results Return from SimX to UVM Scoreboard
simx_run() has returned 0 (success). g_ram[0x90020000] now holds the expected output. Here is how it flows back to the UVM scoreboard.
Step A — UVM calls simx_read_mem() to pull results out of g_ram
// In simx_golden_model::run_phase() (simx_pkg.sv):
byte result_data[];
result_data = new[cfg.data_size]; // allocate SV byte array
simx_read_mem(64'h90020000, // where results are in g_ram
cfg.data_size, // how many bytes to read
result_data); // SV array to fill — inout!
Inside simx_read_mem() (C++):
uint8_t* dest = svGetArrayPtr(data);
g_ram->read(dest, addr, size);
result_data in SV is NOW filled with
the expected bytes — still zero-copy.
Step B — Package result into a UVM transaction and send to scoreboard
// Create transaction object (your project's txn type)
vortex_result_txn expected_txn;
expected_txn = vortex_result_txn::type_id::create('expected_txn');
expected_txn.data = result_data; // the expected bytes
expected_txn.base_addr = 64'h90020000;
expected_txn.is_golden = 1;
result_ap.write(expected_txn); // send to scoreboard
Scoreboard receives from both sides:
← expected (from SimX golden model)
← actual (from RTL monitor)
write_golden(txn) stores expected
write_rtl(txn) stores actual
compare_if_ready() → byte-by-byte
✓ match = PASS
✗ mismatch = UVM_ERROR with addr
Step C — report_phase cleans up C++ objects
function void report_phase(uvm_phase phase);
simx_cleanup(); // delete g_processor, g_ram, g_arch
endfunction // CRITICAL: prevents memory leaks between tests
If simx_cleanup() is skipped: each new test run leaks the old Processor + RAM objects (~4GB virtual). After several tests, the simulation runs out of memory and crashes.

## Slide 25
End-to-End: Complete Call Stack for One Operation
This is what actually happens from top to bottom when your UVM test calls simx_write_mem():
▼
UVM Test (simx_pkg.sv)
simx_write_mem(64'h90000000, 1024, input_A);
SV heap — input_A[] lives here
▼
SV Simulator DPI Dispatch
marshal args → svOpenArrayHandle
trigger dlsym('simx_write_mem') call
QuestaSim internal runtime
▼
DPI-C Runtime Layer
addr=0x90000000, size=1024, handle→svGetArrayPtr
jump to C++ function address in .so
QuestaSim DPI engine
▼
simx_dpi.cpp: simx_write_mem()
uint8_t* src = svGetArrayPtr(data); // ← same bytes as SV array
g_ram->write(src, 0x90000000, 1024);
simx_model.so — in-process
▼
SimX: RAM::write()
page = find_or_create_page(0x90000000);
memcpy(page + offset, src, 1024); // bytes stored
SimX RAM object in heap
▲
Return path
RAM::write returns void
simx_write_mem returns
DPI runtime unwinds args
SV continues next line
Entire round-trip: ~1 microsecond

## Slide 26
Critical Issues to Fix Before Moving Forward
01
CRITICAL — Linker Error
simx_init() Signature Mismatch
Problem: simx_pkg.sv declares: simx_init(string kernel_file, int cores, warps, threads)
simx_dpi.cpp exports: simx_init(int cores, warps, threads) ← NO kernel_file!
→ vsim will fail at runtime: unresolved DPI import symbol
Fix: Option A (Recommended): Remove kernel_file from SV declaration. Add a separate call to simx_load_bin() in run_phase.
Option B: Add const char* kernel_file param to C++ and load binary inside simx_init().
02
BUG — Wrong Execution Mode
Missing simx_run() Import
Problem: simx_pkg.sv calls void'(simx_step(0)) as a run workaround.
simx_step(cycles) advances by N clock cycles — passing 0 literally does nothing!
simx_run() exists in C++ (blocking, runs to completion) but is never declared in SV.
Fix: Add to simx_pkg.sv: import "DPI-C" context function int simx_run();
Replace void'(simx_step(0)) with: ret = simx_run(); in run_phase.
03
IMPORTANT — Config Sync
Makefile -D Defines Must Mirror vortex_config.sv
Problem: -DNUM_CORES=2 -DNUM_WARPS=4 -DNUM_THREADS=4 in Makefile feed SimX at COMPILE TIME.
vortex_config.sv reads the same values at SIMULATION TIME via `ifdef.
If one changes and the other doesn't → SimX models a different processor → false FAIL.
Fix: Create a shared header (vx_sim_params.h) that feeds both, or generate Makefile defines
automatically from the same source as vortex_config.sv parameters.

## Slide 27
Key Takeaways
🏆
SimX is the ONLY correct golden model — same reference the Vortex team uses in CI. Spike/POCL can't model warps.
⚡
C++ golden models are industry standard (ARM/Intel/NVIDIA). 100–1000× faster — runs before RTL even starts.
🔗
DPI-C is a direct binary bridge. Same process, same memory, zero overhead. NOT a translator or code generator.
📁
simx_dpi.cpp owns statics (g_processor/g_ram). svGetArrayPtr() = zero-copy. simx_cleanup() is mandatory.
🔄
Call order: init → load_bin → write_mem × N → dcr_write × N → run → read_mem → ap.write → cleanup.
⚠️
Fix 3 issues NOW: align simx_init() signatures, add simx_run() import, sync Makefile -D defines with config.sv.
Vortex UVM Verification Team · Golden Model: SimX + DPI-C · QuestaSim 2021 / Ubuntu 22.04 · v2 — Deep Guide